## Slide 1: Wireless

## Slide 2: Mobile/Wireless Node Structure
Classifier:Forwarding
Agent: Protocol Entity
Node Entry
Node
ARP
Radio Propagation Model
MobileNode
LL
MAC
PHY
LL
CHANNEL
LL
MAC
LL:Link layer object
IFQ:Interface queue
MAC:Mac object
PHY
PHY:Net interface
Routing

## Slide 3: Wireless Simulation Script
set val(chan) Channel/WirelessChannel ;# channel type
set val(prop) Propagation/TwoRayGround ;# radio-propagation model
set val(netif) Phy/WirelessPhy ;# network interface type
set val(mac) Mac/802_11 ;# MAC type
set val(ifq) Queue/DropTail/PriQueue ;# interface queue type
set val(ll) LL ;# link layer type
set val(ant) Antenna/OmniAntenna ;# antenna model
set val(ifqlen) 50 ;# max packet in ifq
set val(nn) 3 ;# number of mobilenodes
set val(rp) AODV ;# routing protocol
set val(x) 500 ;# X dimension of topography
set val(y) 400 ;# Y dimension of topography
set val(stop) 110 ;# time of simulation end

## Slide 4: Wireless Simulation Script (contd ….)
#Create a ns simulator
set ns [new Simulator]
#Setup topography object
set topo [new Topography]
$topo load_flatgrid $val(x) $val(y)
create-god $val(nn)
#Open the NS trace file
set tracefile [open wireless.tr w]
$ns trace-all $tracefile
#Open the NAM trace file
set namfile [open wireless.nam w]
$ns namtrace-all $namfile
$ns namtrace-all-wireless $namfile $val(x) $val(y)
set chan [new $val(chan)] ;#Create wireless channel

## Slide 5: Wireless Simulation Script (contd ….)
# Mobile Node Parameter Setup(configuration of instances)
$ns node-config -adhocRouting $val(rp) \
-llType $val(ll) \
-macType $val(mac) \
-ifqType $val(ifq) \
-ifqLen $val(ifqlen) \
-antType $val(ant) \
-propType $val(prop) \
-phyType $val(netif) \
-channel $chan \
-topoInstance $topo \
-agentTrace OFF \
-routerTrace OFF\
-macTrace ON \
-movementTrace ON

## Slide 6: Wireless Simulation Script (contd ….)
#Create 3 nodes
  for {set i 0} {$i < $val(nn) } { incr i } {
  set node_($i) [$ns node]
  }
  # Provide location of mobile nodes
  $node_(0) set X_ 5.0
  $node_(0) set Y_ 5.0
  $node_(0) set Z_ 0.0
  $node_(1) set X_ 490.0
  $node_(1) set Y_ 285.0
  $node_(1) set Z_ 0.0
$node_(2) set X_ 150.0
$node_(2) set Y_ 240.0
$node_(2) set Z_ 0.0

## Slide 7: Wireless Simulation Script (contd ….)
# Generation of movements
  $ns at 10.0 "$node_(0) setdest 250.0 250.0 3.0"
  $ns at 15.0 "$node_(1) setdest 45.0 285.0 5.0"
  $ns at 110.0 "$node_(0) setdest 480.0 300.0 5.0"

## Slide 8: Wireless Simulation Script (contd ….)
# Set a TCP connection between node_(0) and node_(1)
  set udp [new Agent/UDP]
  set sink [new Agent/Null]
  $ns attach-agent $node_(0) $udp
  $ns attach-agent $node_(1) $sink
  $ns connect $udp $sink
  set cbr [new Application/Traffic/CBR]
  $cbr attach-agent $udp
  $cbr set interval_ 1
  $cbr set maxpkts_ 100
  $ns at 10.0 "$cbr start"

## Slide 9: Wireless Simulation Script (contd ….)
# Define node initial position in nam
  for {set i 0} {$i < $val(nn)} { incr i } {
  # 30 defines the node size for nam
  $ns initial_node_pos $node_($i) 30
  }
# Telling nodes when the simulation ends
  for {set i 0} {$i < $val(nn) } { incr i } {
  $ns at $val(stop) "$node_($i) reset";
  }

## Slide 10: Wireless Simulation Script (contd ….)
# Ending nam and the simulation
  $ns at $val(stop) "$ns nam-end-wireless $val(stop)"
  $ns at $val(stop) "stop"
  $ns at 110.01 "puts \"end simulation\" ; $ns halt“
  # Stop Procedure
  proc stop {} {
  global ns tracefd namtrace
  $ns flush-trace
  close $tracefd
  close $namtrace
  }
# Run simulation
$ns run
wireless1.tcl

## Slide 11: WSN Simulation
# Define Options
  set val(chan) Channel/WirelessChannel ;# channel type
  set val(prop) Propagation/TwoRayGround ;# radio-propagation model
  set val(netif) Phy/WirelessPhy ;# network interface type
  set val(mac) Mac/802_11 ;# MAC type
  set val(ifq) Queue/DropTail/PriQueue ;# interface queue type
  set val(ll) LL ;# link layer type
  set val(ant) Antenna/OmniAntenna ;# antenna model
  set val(ifqlen) 100 ;# max packet in ifq
  set val(nn) 20 ;# number of mobilenodes
  set val(rp) AODV ;# protocol tye
  set val(x) 50 ;# X dimension of topography
  set val(y) 50 ;# Y dimension of topography
  set val(stop) 500 ;# simulation period

## Slide 12: WSN Simulation (contd…)
# Energy Parameters
  set val(energymodel) EnergyModel
  set val(initialenergy) 100
# Simulator Objects and File Descriptor
  set ns [new Simulator]
  set tracefd [open sim_802_11.tr w]
  set namtrace [open sim_802_11.nam w]
  $ns trace-all $tracefd
  $ns namtrace-all-wireless $namtrace $val(x) $val(y)
  # Set up topography object
  set topo [new Topography]
  $topo load_flatgrid $val(x) $val(y)
  # Create Node Instance
  create-god $val(nn)

## Slide 13: WSN Simulation (contd…)
  # configure the node instance
  $ns node-config -adhocRouting $val(rp) \
  -llType $val(ll) \
  -macType $val(mac) \
  -ifqType $val(ifq) \
  -ifqLen $val(ifqlen) \
  -antType $val(ant) \
  -propType $val(prop) \
  -phyType $val(netif) \
  -channel [new $val(chan)] \
  -topoInstance $topo \
  -agentTrace OFF \
  -routerTrace OFF \
  -macTrace ON \
  -movementTrace OFF \
  -energyModel $val(energymodel) \
  -initialEnergy $val(initialenergy) \
  -rxPower 35.28e-3 \
  -txPower 31.32e-3 \
  -idlePower 712e-6 \
  -sleepPower 144e-9

## Slide 14: WSN Simulation (contd…)
# Create Nodes
  for {set i 0} {$i < $val(nn) } { incr i } {
  set mnode_($i) [$ns node]
  }
# Positions of Source Nodes
  for {set i 1} {$i < $val(nn) } { incr i } {
  $mnode_($i) set X_ [ expr {$val(x) * rand()} ]
  $mnode_($i) set Y_ [ expr {$val(y) * rand()} ]
  $mnode_($i) set Z_ 0
  }
# Position of Sink
  $mnode_(0) set X_ [ expr {$val(x)/2} ]
  $mnode_(0) set Y_ [ expr {$val(y)/2} ]
  $mnode_(0) set Z_ 0.0
  $mnode_(0) label "Sink"

## Slide 15: WSN Simulation (contd…)
# Initial Position in NAM
  for {set i 0} {$i < $val(nn)} { incr i } {
  $ns initial_node_pos $mnode_($i) 10
  }
#Create UDP Agents
  for {set i 1} {$i < $val(nn) } { incr i } {
  set udp($i) [new Agent/UDP]
  $ns attach-agent $mnode_($i) $udp($i)
  }
# Create Null Agent
  set sink [new Agent/Null]
  $ns attach-agent $mnode_(0) $sink
# Connect Source to Sink
  for {set i 1} {$i < $val(nn) } { incr i }
  {
  $ns connect $udp($i) $sink
  }

## Slide 16: WSN Simulation (contd…)
# Setup a CBR over UDP connection
  for {set i 1} {$i < $val(nn) } { incr i } {
  set cbr($i) [new Application/Traffic/CBR]
  $cbr($i) attach-agent $udp($i)
  $cbr($i) set type_ CBR
  $cbr($i) set packet_size_ 100
  $cbr($i) set maxpkts_ 100
  $cbr($i) set interval_ 1}
# Start CBR Traffic
  for {set i 1} {$i < $val(nn) } { incr i } {
  $ns at [expr {$i + 5}] "$cbr($i) start"}
# Stop CBR Traffic
  for {set i 1} {$i < $val(nn) } { incr i } {
  $ns at [expr $val(stop) - $i] "$cbr($i) stop"
  }

## Slide 17: WSN Simulation (contd…)
# Telling nodes when the simulation ends
  for {set i 0} {$i < $val(nn) } { incr i } {
  $ns at $val(stop) "$mnode_($i) reset;"
  }
# ending nam and the simulation
  $ns at $val(stop) "$ns nam-end-wireless $val(stop)"
  $ns at $val(stop) "stop"
  $ns at [expr $val(stop) + 0.01] "puts \"end simulation\"; $ns halt"
  proc stop {} {
  global ns tracefd namtrace
  $ns flush-trace
  close $tracefd
  close $namtrace
  }
$ns run
802_11_wsn.tcl